## Slide 1: Locating VH-MDX
Glenn Strkalj
Glenn Horrocks
BWRS
21st August 2015

## Slide 2: TOPICS
Clarification of BWRS position to VH-MDX
Research update
Most Probable Area (MPA)
Research direction
New website

## Slide 3: SCOPE
The last brief was more to demonstrate the complexity and unknowns and to take people ‘off the rails’ and ‘unfreeze’ conclusions
This one: more of a brief to you of our activities
Limited time
Limited questions

## Slide 4: BWRS POSITION
Complete original mission from 1981: Locate VH-MDX
Do not wish to engage in political, legal or self-interest based activities
Proliferate accurate VH-MDX information.

## Slide 5: RESEARCH UPDATE
Much new information (as always)
Many new sources
Important findings
Only a very small selection will be briefly overviewed

## Slide 6: ASIB/RCC final WLM radar position

## Slide 7: ASIB/RCC final WLM radar position
Unlikely a radar fade position: why?
  WLM ATCO: states no paint fade observed
  Radar propagation results do not align with likely altitudes leading into and at the position
  Other information suggests a more easterly track
Likely to be the plot of a radar vectored aircraft post accident to the 320˚M/45NM fix
Likely to have ‘morphed’ into a fade position through ‘Chinese whispers’
Believed by us to be the 320˚M/45NM position miss-interpreted as a fade position
This position will be reviewed continually.

## Slide 8: ASIB/RCC final WLM radar position
1. Initially a pure 320˚M/45NM WLM position was specified as MPP (10 Aug 81)
2. 2nd day after the accident comms between WLM and SYD refine the MPP to here
(11 Aug 81)
4. In 2014 we define the 320˚M/45NM position as here
3. Within 2 weeks of the accident, helicopters were radar vectored by WLM to the ‘final WLM’ position
We think points in the orange circle represent the same radar position (WLM 320˚M/45NM 0936:00UTC).
But not a radar fade position!

## Slide 9: Sydney deposed final radar position

## Slide 10: Sydney deposed final radar position
Information found that questions the true nature of this position
Still valid to suggest eastward tracking
Defensible enough at this stage to offer a general area for the final observed radar paint
Sydney ATC did observe radar fade
Newly found information suggests Sydney radar fade at approximately 330˚M/45NM WLM

## Slide 11: Mosaic gating line
The Round Mountain (TRM) SSR Paints only north of line
Sydney (SYD) SSR Paints only south of line

## Slide 12: Mosaic gating line
Prevents two Secondary Surveillance Radar (SSR) symbols being displayed for same aircraft (from two radar sources)
One SSR source for each display section
A simple system; above the line (north) only The Round Mountain (TRM) Route Surveillance Radar (RSR) derived SSR symbols displayed
Below the line (south) only Sydney RSR derived SSR symbols displayed
Unknown if Primary Surveillance Radar (PSR) used the same gate (very useful if so); looking into it.

## Slide 13: Final radar observed track
Final SYD radar track of VH-MDX obtained from two sources
Both sources of good reliability
Exact starting position of track unclear
Suggests an E-N-E track from 320˚M/45NM
Corroborates with other information

## Slide 14: MOST PROBABLE AREA (MPA)
MPA reflects the most probable area(s) that current information, data and interpretation suggest VH-MDX is located within
Will change with time

## Slide 15: Flight path: What do we think?
Accumulated ice
Turned south
Then a slow turn to a E-N-E final track
Accumulated more ice
Either maintained lateral control to impact or fully departed controlled flight after the 5000’ call (both feasible)
Assuming VH-MDX slowed from cruise to climb speed in the final minutes

## Slide 16
Depicted flight path is approximate to show general tracking trend

## Slide 17: Why E-N-E?
1x SYD and WLM ATCO ‘feel’ an easterly track
1x SYD ATCO deposed final posit to the east
SYD fade recorded as ≈330˚M/45NM WLM
E-N-E final tracks suggested by two sources
1x ATCO recalls slow turn to east
Gloucester, Taree and Foster townships
VH-MDX may have ended up on lee of cloud
≈0934UTC VH-MDX likely >48NM WLM to W so, flew ‘into’ radar display (easterly track)

## Slide 18: Deviations and statistical distribution
All data is subject to deviation: a measurement is rarely pure
Deviation values are contingent on:
  The way it was measured
  What tools were used to measure it
So, 320˚M at the 0936UTC fix may be:
  310˚M-330˚M if assessed quickly
  315˚M-325˚M if assessed with some care
  318˚M-322˚M if assessed with prudence

## Slide 19: Stochastic Analysis
Too simple:
“X” never marks the spot
There is uncertainty in range
There is uncertainty in direction
These combine to give a probability distribution
The stochastic approach also includes other uncertainties:
wind speed and direction
radar accuracy
aircraft speed and direction
crash time

## Slide 20: Deviations and statistical distributions
To obtain an area representing where VH-MDX is most probably within, statistical distribution must be applied
Distributions are based on specification tolerance values or best assumptions
Constant refinement of deviation values

## Slide 21: MPA Parameters
Starting point: 324˚M/46NM +/-1˚, +/-1NM
Starting time: 0936:00UTC +/-10 seconds
Track group 1: 060˚ - 080˚
Track group 2: 324˚M/46NM to deposed final position
Speed range: 130KIAS slowing linearly to 90KIAS
Time of flight: last call + 30 seconds
Assumption at ‘five thousand’ call: straight, current track
If VH-MDX spun or spiraled instead of a straight track, the relatively small turn radii would generally be contained by the MPA area
Wind: Area forecast winds modeled for effects of Upper Williams River area terrain (will be updated to Gloucester Tops terrain when time available).

## Slide 23: 1st area: Radar Fade
Fade time 0938:30-0939:00UTC
Add deviations and plot DR tracks
Expected radar fade altitude (from transcripts) = 5900’-6400’AMSL
Radar propagation suggests 6000’-6400’ AMSL minimum interrogation altitudes : so corroborates.
Area fits inside Sydney radar fade position (330˚M/45NM WLM +/-5˚) (orange line is 330˚M WLM, red 335˚M WLM, bottom grey line is 45NM WLM)
Centre bearing of area ≈334˚M WLM
VH-MDX radar observed to slow. Why?:
    Spin
    Spiral (therefore turning in tight radius)
    Climb profile (slower speed)
    Turned into wind

## Slide 24: 2nd area: 5000’ altitude
Why important?: audio suggests lateral control likely maintained till this call
After this: a spin or spiral dive is viewed possible.
Why? The pilot likely tried to climb and this increases the chance of loss of control of aircraft (e.g. stall/spin)

## Slide 25: 3rd area: Straight track impact
Last received radio call + 30 sec
Straight tracks from 324˚M/46NM
Add deviations and plot DR tracks

## Slide 26: What does all this mean?
We think VH-MDX is located in the green boxes.
We currently think VH-MDX is most probably located within the three stochastic areas depicted.
From the three stochastic areas we can consider options to flight path and select search areas.
Choose area for scenario e.g.:
5000’ area for departed flight (spin, spiral dive)
Straight track impact area for maintenance of lateral control to impact.
Be ready for change!!!

## Slide 27: Resulting areas
Three areas (Radar fade, 5000’, Impact): ≈56 sqkm
Highest probability areas (blue) connected: ≈19 sqkm
In anticipation of this MPA, BWRS has conducted recce and small scale activities in the area since 2014
Land search not really applied to the area by emergency services
Not a focus area during the 1980’s searches
Steep terrain
Significant low lying vegetation
‘Dry’ area (take in water)
Tiger snakes!!

## Slide 28: RESEARCH DIRECTION
Continue in the current direction
Continual refinement
Our research is now sufficient to support involvement of universities in key areas (radar, GIS etc.)
Our research is now sufficient to start looking at remote sensing options

## Slide 29: NEW WEBSITE
www.vhmdx.com.au
A dedicated website to locating VH-MDX
Central point for:
  Research information
  Search track records
  Information sharing
  Proliferating accurate VH-MDX information
Forum for discussion (no political, self-interest or legal type discussions)

## Slide 30: The End