## Slide 1: Locating VH-MDX
Glenn Strkalj BWRS
December 2014
Image: G. Strkalj 2014

## Slide 2: Objectives
Brief members on individual research conducted by myself and Glenn Horrocks
Clarify particular aspects of the VH-MDX event
Brief members on recent and future BWRS/WICEN/VRA VH-MDX activities
Motivate organisations and individuals
Form ‘one team’
Why are we here?

## Slide 3: Topics
Overview of where BWRS are at with VH-MDX research
Clarify some aviation concepts to non-aviation types
Briefly overview remote sensing techniques being used and considered

## Slide 4: Scope
A quick overview of many aspects
Not all questions can be answered in depth as a result of timeframe

## Slide 5: Research
Tear Down Approach
Attention to detail
Unfreeze/ new areas/ different directions
Question everything
No fear in backtracking and amending: if something can be ‘fixed’ it will be
There will be failures: this is good as we only get stronger
Critical research will find VH-MDX!

## Slide 6: Aircraft
Cessna 210M Centurion
High Wing
Metal construction (Aluminum)
Piston engine
Approx 1.7 Tonnes at Max weight
11.2m wing span, 8.6m fuselage length
6 seats available, 5 persons were on board
Approx 180L of fuel on board during impact

## Slide 7
Image: Cessna aircraft company 1976

## Slide 8
Image: G. Strkalj 2014

## Slide 10
Image: G. Strkalj 2014

## Slide 11: Weather
Contrary to popular belief: Predominately clear skies!
Dark Night
A cold front had passed approx 9 hours previously
Strong south-westerly to westerly winds
Localised orographic cloud over mountain ranges
Turbulence along coast associated with flow over the Great Dividing Range

## Slide 12
Orographic Cloud Formation

## Slide 13: Primary ATS Agencies Involved
Sydney Flight Information Service 5 (SY FIS-5) (FS is not ATC) Probably 2x Flight Service Officers (FSO’s)
Sydney Sector 1: 1 x ATCO on duty, 1x SAAC who was almost immediately involved, 1x ATCO who joined in
RAAF Williamtown ATC: 1x ATCO on duty conducting procedural control but with radar on for extra SA.

## Slide 14: Planned and Actual Flight Path
All cool until Taree
From Taree planned to track to Craven waypoint
Craven waypoint is approximately 17.5km west of Craven township! (2km south of Mt Berrico)
Craven waypoint is defined by the intersection of two beacon (navaid) bearings
There was no beacon or specific ground feature at Craven waypoint
Image: Australian Government (Department of Transport 1981).

## Slide 15
Craven Waypoint
Mt Berrico
Craven Township
Image: OzRunways 2014, Additions: G. Strkalj

## Slide 16
Image: Bennett Avionics 2001-2014
Image: Bennett Avionics 2001-2014
Image: Australian Government (Department of Transport 1981).
Image: G. Strkalj 2014

## Slide 17
VH-MDX offered a clearance through Williamtown airspace by Sydney FIS-5
Clearance offered by RAAF Williamtown almost immediately
Clearance delayed by Sydney ATS due unknown weather in adjoining Sydney airspace
Airspace clearances

## Slide 18
VH-MDX proceeded to track west of intended track
Entered some of the only cloud in the region
Reported loss of primary attitude and heading instrumentation
Experienced significant turbulence then icing
Decision to track inland

## Slide 19
Image: Australian Government (Department of Transport 1981).

## Slide 20: Radar: Two Technologies
Images: Dick Barrett 2000-2002

## Slide 21
Primary Surveillance Radar (PSR):
-‘Bouncing’ a radio signal off an aircraft
- Reliant on aircraft physical characteristics (shape, materials, aspect, geometry etc)
Images: Dick Barrett 2000-2002

## Slide 22
Secondary Surveillance Radar (SSR):
-‘Talking’ to a piece of aircraft equipment
- Not reliant aircraft physical characteristics
- A ‘conversation’
is taking place
Image: Dick Barrett 2000-2002
Image: Bennett Avionics 2001-2014

## Slide 23
(Photo: Fighter World Aviation Museum 2014).

## Slide 24
Examples of Radar Paints
Photo: M. Price c.1983
Photo: H. Howard c.1983

## Slide 25
Image: Australian Government

## Slide 26: Radar Propagation
PSR and SSR transmissions are broad in elevation and very narrow in azimuth
Line of sight
Image: Nizhny Novgorod Research Institute of Radio Engineering (NNIIRT)
cited in Air Power Australia 2008

## Slide 27: Propagation Analysis
Image: RadioMobile Online, analysis: G. Strkalj 2014

## Slide 28: Radars Involved (3x)
Sydney Route Surveillance Radar (RSR) (Located at Sydney Airport)
The Round Mountain RSR (Located west of Coffs Harbour)
RAAF Williamtown SURAD Terminal Approach Radar (TAR) (Located at RAAF Williamtown, north of Newcastle)

## Slide 29
Image: UBD Gregory's Australia

## Slide 30
Sydney ‘Northern Mosaic’ Display
Image: Australian Government c.1981

## Slide 31
Sydney ‘Northern Mosaic’ Display
Image: M. Price c.1983

## Slide 32
Melbourne AACC
Image: Australian Government, Courtesy of Airways Museum

## Slide 33
Image: Australian Government (Royal Australian Air Force)

## Slide 34: SURAD PPI
SURAD Controls
Image: H. Howard c.1983

## Slide 35: Radar Display Persistence (Paint Fade Time)
WLM SURAD Persistence 1-5 sweeps = 4-20 seconds
Sydney: Not confirmed at this stage
When WLM ATCO checked radar display (PPI) at 0941:10Z there were no VH-MDX paints
A thorough check was conducted at 0941:20Z with no VH-MDX paints observed
Final received transmission from VH-MDX was at 0939:26Z

## Slide 36: Specific Williamtown Radar Positions
Only one positive confirmed fix at 320M/45NM at 0936:00Z
A likely radar observation at 0938:30Z of VH-MDX on the 330M bearing from WLM probably by WLM but maybe SYD
The Williamtown ATCO did NOT observe final radar fade of VH-MDX

## Slide 37: 320M/45NM Fix: 0936:00Z
ATCO was conducting his primary procedural control duties away from the PPI
ATCO stepped over to the PPI and observed the ident triangle and an SSR symbol, most likely a circle, in the 320/45 position
A rule off was not required as the paints were so close to the PPI outer edge where the compass rose was
SSR symbols were variable in size as preset by technicians but around 1NM size would be minimum
ATCO confident within +/-2 deg
SSR symbols were not clipped by the 48NM outer edge of PPI nor were they hanging over the 44NM MTI boundary: this means VH-MDX was between 45NM and 47NM
Image: G. Strkalj 2014

## Slide 38: 320M/45NM Fix: 0936:00Z
Regardless of whether VH-MDX was squawking Mode A SSR code 4000 or 3000 the Sydney and Williamtown ATC radars could interrogate and display either of the received squawk codes
WLM tower radar display (PPI) was set to 48NM maximum range
Accordingly, just after 0934:00Z VH-MDX was likely outside 48NM WLM
This can elude to aircraft speed and limit approach tracks into the 320/45NM position

## Slide 39: Specific Sydney Radar Positions
Initial position 36NM north of Singleton, slightly west of the Singleton-Mount Sandon Track (SSR Ident) @ 0928:28Z
320M/46NM from Williamtown @ 0934:30Z
Final position approximately 5NM west of Craven waypoint most likely around 0939:00Z

## Slide 40
Base plot: Australian Government (Department of Transport) 1981, additions: G. Strkalj 2014)

## Slide 41: Final Position by Williamtown Radar: ASIB/RCC Position c.1981
Included in the Sep 1981? Accident Investigation Summary Report
No base bearing/range information
WLM ATCO did not observe paint fade
No confirmation of originating authority
There was no radar track recording capability at Sydney or WLM
WLM ATCO does not recall being interviewed by ASIB
Propagation wise possible down to approx 3500’AMSL
Where did this originate from??????
Images: Australian Government (Department of Transport) 1981

## Slide 42: Final Position by Williamtown Radar: BASI c.1983
This is the 320M/45NM position at 0936:00Z
Note that the ASIB/RCC final radar position is not referred to in this Accident Investigation Summary Report (1983)
Also note that reference specifically to ‘Williamtown’ radar for the final radar fade position is removed in 1983 compared to Sep 1981
Images: Australian Government (Bureau of Air Safety Investigation) 1983

## Slide 43: Final Radar Position Sydney ATC
ATCO’s were continually looking at the radar display
Radar fade was confidently observed by at least 1 x ATCO
An ASIB officer was reasonably sure that ATCO’s did observe the paint fade -The final position aligns with Sector 1 ATCO’s assertion of an easterly track from 320/45
Communications signal strength increase with time loosely backs up the position
No time of final position although comms transcripts suggest 0939:00Z
The pilot reported the coast in sight and was likely to continue tracking for the coast (east)
Images: Australian Government (Department of Transport) 1981

## Slide 44: Conclusions: Last Radar Positions:
ASIB/RCC and Sydney last radar positions are separated by approximately 10NM
This is considered well outside expected normal radar tolerances
Normal radar tolerances (technical) are within hundreds of meters
So one of these last radar positions is ‘correct’ the other not
WHICH ONE?

## Slide 45
Image: G. Strkalj 2014

## Slide 46
192KTAS max power descent
6 minutes
Tracking in all directions from 320˚M/45NM radar fix
+/-10˚ azimuth tolerance at 320˚M/45NM radar fix
+3NM/-1NM range tolerance at 320˚M/45NM radar fix
Wind 225˚M-270˚M 30-80 knots

## Slide 47
Most Likely Extent
- 122 KTAS Normal Climb
172 KTAS Cruise Speed
≈+1 minute after final radio call
Tracking in easterly hemisphere
+/-2˚ azimuth tolerance at 320˚M/45NM radar fix
+2NM/-0NM range tolerance at 320˚M/45NM radar fix
Wind 225˚M-270˚M 30-50 knots
Image: G. Horrocks & G. Strkalj & 2014

## Slide 48: Mapping All Searches
Big job
Needs to be done correctly

## Slide 49: Questions?